# Load
## Instructions
LDW, LDB, LDH, TLBWRITE, LI

## Fetch
The PC is translated to a PHA (can cause a TLB miss).
If PHA translated, try to retrieve the inst from cache (can cause cache miss).
Then the result from the cache is written in the f_instr_input.

## Decode
In translate opcode to calc_func.
For TLBWRITE, only r_d_a is decoded which is either 0 (ITLB miss) or 1 (DTLB miss), the rst of the iinstruction is ignored.
For LI r_a_in is the value. For LDW, LDB & LDH try_to_bypass or get the value from RF if possible. For LDW, LDB & LDH r_b is the offset of the instruction and r_d_a is the register number to load to. Stld_size_in (size of the result of operation) is also needed to get the size the instruction is working with (W, H, B).

## ALU
LDW, LDB & LDH r_a + r_b (r_b is the offset) is calculated and stored in res_in, this is the memory address
TLBWRITE: rm4 needs to be 1 to ensure that the privileges are given. For an itlb miss write rm1 into the itlb. For a dtlb miss write rm1 into the dtlb.
LI: res_in is r_a, which is the integer value that should be loaded in the target register.
## Cache
In the cache the address is translated. For LDW, LDB & LDH the line is looked up in the cache (and if needed retrieved from mem), and written in res_in.
For LI and TLBWRITE noting happens.

## WB
For LI, LDW, LDB & LDH the result of res is written in the register r_d_a.
For TLBWRITE nothing happens because it has already done its job.
I/DTLB misses are handled here.

# Store
## Instructions
STW, STB, STH

## Fetch
It is the same as for the loads.

## Decode
Calcualte the f_func. then load the first reg in r_a and the offset in r_b, load the register to save from into r_d_a_val.
Calculate stld_size to indicate how big the data to save is.

## ALU
r_a + r_b (r_b is the offset) is calculated and stored in res_in, this is the memory address, to store to.

## Cache
The address from res is translated to PHA, then looked up in the cache. Then if everything worked r_d_a_val is stored in the correct cache line.

## WB
Nothing to write back.
I/DTLB misses are handled here.

# Branch / Jump
## Instructions
JUMP, BEQ, IRET

## Fetch
Same as always
## Decode
Calcualte the function value for the alu (Jump = 4, BEQ = 3, IRET = 33).
For JUMP save the base address in r_d_a and the offset in r_b.
For BEQ save the first register to compare in r_a the second in r_d_a_val. The offset is the saved in r_d_b (and will be interpreted as an absolute address and also translated).
For IRET don’t decode anything.
## ALU
For JUMP add the r_d_a to signed(r_b) and jump to that address.
For BEQ if r_a == rd_a_val jump to r_b else don’t jump.
IRET swaps the rm4 registers to change the privalages, then puts rm0 in a_res_in which is the jump goal.
## Cache
In the cache if there is a jump a_jump is set and the pc is switched to to a_res.
Also nop every younger instruction to make sure they don’t affect the state.
If swap_rm4 is true, set rm4 to 0 and clean irm1 and irm0.

## WB
Nothing is done in the write back stage.

# Arithmetic
## Instructions
SUB, MUL, ADD

## Fetch
Same as always

## Decode
The func value that should be executed in the Alu is calculated. The values for r_a and r_b are retrieved and possibly bypassed (or dependencies in pipeline but not bypassable, then stall). Then the target register address is saved in r_d_a.

## ALU
Do the calculations. For Sub: r_a – r_b, Add: r_a+ r_b, Mul: r_a * r_b. Save the result in res.

## M1 – M5
Go trough the stages.
Because we didn’t get the rob to work, stall the pipeline until the mull stages are finished, unless the instruction in decode is a mul than than don’t stall.

## Cache
In the cache stage there is nothing to do.

## WB
Set the register at number r_d_a to the value of res.

# Exc
## Fetch
When a ITLB miss occurs the exception is set to 1.
## Decode
If a exception is present in the f_exception ff, set the instruciton curently in F stage to be a nop.
## ALU
If a exception is present in the d_exception ff, set the instruciton curently in F & D stage to be a nop.
## Cache
If a exception is present in the a_exception ff, set the instruciton curently in F, D & A stage to be a nop.
If a DTLB miss happens then c_exception_in is set to 2. This doesn’t overwrite the ITLB miss, because when an ITLB miss happens there is no instruction set, thus it is a Add which can’t have a DLTB miss.
## WB
In the write back stage the exception is checked. If it is 1 then jump to 2000 and set rm0 = irm0 and rm1 = irm1. If it is 2 then jump to 2010 and set rm0 = drm0 and rm1 = drn1. Also make sure that all instructions currently in the pipeline are noped, that they don’t change anything the os can safly jump back to the falting instruction.
## ROB
## Fetch
Set tail_in = tail + 1. If the tail_in == rob_head than the ROB is full.

## ALU
If the instruction is finished in alu wirte the result to the rob and set it to valid.
## Cache
If the instruction is a store or load, then it is finished after the cache stage and can be written to the rob.
# WB
# If the entry at rob_head is valid, handle it’s eceptions. If no exceptions exist save it in the cache or in in the registers.
## Performance results
Buffer sum:
Mem copy:
Matrix mult: