# Load
## Instructions
LDW, LDB, LDH, TLBWRITE, LI

## Fetch
The PC is translated to a PHA (can cause a TLB miss).
If PHA translated, try to retrieve the inst from cache (can cause cache miss).
Then the result from the cache is written in the f_instr_input.

## Decode
In translate opcode to calc_func.
For TLBWRITE, only r_d_a is decoded which is either 0 (ITLB miss) or 1 (DTLB miss), the rst of the instruction is ignored.
For LI r_a_in is the value. For LDW, LDB & LDH try_to_bypass or get the value from RF if possible. For LDW, LDB & LDH r_b is the offset of the instruction and r_d_a is the register number to load to. Stld_size_in (size of the result of operation) is also needed to get the size the instruction is working with (W, H, B).

## ALU
LDW, LDB & LDH r_a + r_b (r_b is the offset) is calculated and stored in res_in, this is the memory address
TLBWRITE: rm4 needs to be 1 to ensure that the privileges are given. For an itlb miss write rm1 into the itlb. For a dtlb miss write rm1 into the dtlb.
LI: res_in is r_a, which is the integer value that should be loaded in the target register.
## Cache
In the cache the address is translated. For LDW, LDB & LDH the line is looked up in the cache (and if needed retrieved from mem), and written in res_in.
For LI and TLBWRITE noting happens.

## WB
For LI, LDW, LDB & LDH the result of res is written in the register r_d_a.
For TLBWRITE nothing happens because it has already done its job.
I/DTLB misses are handled here.

# Store
## Instructions
STW, STB, STH

## Fetch
It is the same as for the loads.

## Decode
Calculate the f_func. then load the first reg in r_a and the offset in r_b, load the register to save from into r_d_a_val.
Calculate stld_size to indicate how big the data to save is.

## ALU
r_a + r_b (r_b is the offset) is calculated and stored in res_in, this is the memory address, to store to.

## Cache
The address from res is translated to PHA, then looked up in the cache. Then if everything worked r_d_a_val is stored in the correct cache line.

## WB
Nothing to write back.
I/DTLB misses are handled here.

# Branch / Jump
## Instructions
JUMP, BEQ, IRET

## Fetch
Check if the PC is known by the BP (Branch Predictor) and if it should jump.
If no do the same as always. If yes jump to the predicted address (real jumps have priority because they are from an older instruction and the current instruction in fetch wouldn’t survive).
## Decode
Calculate the function value for the alu (Jump = 4, BEQ = 3, IRET = 33).
For JUMP save the base address in r_d_a and the offset in r_b.
For BEQ save the first register to compare in r_a the second in r_d_a_val. The offset is the saved in r_d_b (and will be interpreted as an absolute address and also translated).
For IRET don’t decode anything.
## ALU
For JUMP add the r_d_a to signed(r_b) if the prediction was already to this address do nothing else jump to that address.
For BEQ if r_a == rd_a_val jump to r_b else don’t jump (also Check if the resulting address is the predicted one else jump to correct address).
IRET swaps the rm4 registers to change the privileges, then puts rm0 in a_res_in which is the jump goal.

## Cache
In the cache if there is a jump a_jump is set and the pc is switched to to a_res.
Also nop every younger instruction to make sure they don’t affect the state.
If swap_rm4 is true, set rm4 to 0 and clean irm1 and irm0.

## WB
Nothing is done in the write back stage.

# Arithmetic
## Instructions
SUB, MUL, ADD

## Fetch
Same as always

## Decode
The func value that should be executed in the Alu is calculated. The values for r_a and r_b are retrieved and possibly bypassed (or dependencies in pipeline but not bypassable, then stall). Then the target register address is saved in r_d_a.

## ALU
Do the calculations. For Sub: r_a – r_b, Add: r_a+ r_b, Mul: r_a * r_b. Save the result in res.

## M1 – M5
Go trough the stages.
Because we didn’t get the rob to work, stall the pipeline until the mull stages are finished. If M5 is reached the Pipeline continues.

## Cache
In the cache stage there is nothing to do.

## WB
Set the register at number r_d_a to the value of res.

# Exc
## Fetch
When a ITLB miss occurs the exception is set to 1.
## Decode
If a exception is present in the f_exception ff, set the instruciton curently in F stage to be a nop.
## ALU
If a exception is present in the d_exception ff, set the instruciton curently in F & D stage to be a nop.
## Cache
If a exception is present in the a_exception ff, set the instruciton curently in F, D & A stage to be a nop.
If a DTLB miss happens then c_exception_in is set to 2. This doesn’t overwrite the ITLB miss, because when an ITLB miss happens there is no instruction set, thus it is a Add which can’t have a DLTB miss.
## WB
In the write back stage the exception is checked. If it is 1 then jump to 2000 and set rm0 = irm0 and rm1 = irm1. If it is 2 then jump to 2010 and set rm0 = drm0 and rm1 = drn1. Also make sure that all instructions currently in the pipeline are noped, that they don’t change anything the os can safly jump back to the falting instruction.
## ROB
## Fetch
Set tail_in = tail + 1. If the tail_in == rob_head than the ROB is full.

## ALU
If the instruction is finished in alu wirte the result to the rob and set it to valid.
## Cache
If the instruction is a store or load, then it is finished after the cache stage and can be written to the rob.
# WB
# If the entry at rob_head is valid, handle it’s eceptions. If no exceptions exist save it in the cache or in in the registers.
## Performance results
Buffer sum:
1403
Mem copy:
2363
Matrix mult:

With: 8*8*8 15098
Buffer Mul:
2173